Target Specification for PA600 Power Amp

Parameter	Target	Compliance

Band coverage	160 - 6m	Yes
Power output	P1dB >600W on all bands	Yes
IMD3	<-30dB(PEP)	Yes
Spurious	<-46dBc, 160-10m / <-70dBc, 6m	Yes
Input VSWR	<1.5	Yes
Drive power	options for 5W, 10W or 50W PEP input	Yes
Output VSWR	<1.5	Yes
Gain variation	<3.0dB across 160 - 10m	TBD
Antenna ports	2	Yes
Rating	Continuous transmit: / - 600W SSB/CW / - 300W RTTY/data / Intermittent transmit: / - 600W key down for 5 minutes key down followed by 5 minutes rest	Yes
Band selection	Manual / Automatic based on transmit frequency / Icom C-IV interface / Icom Analogue band control	Yes / Yes / Yes / Yes
Operator interface	4.3 inch or larger touch panel	Yes
Metering	Idd, Vdd, output power, VSWR, temperature	Yes
Safety protection	Over-current, over-temperature, high VSWR, excess drive, wrong band selection	Yes

Remote operation	WiFi	TBD

Acoustic noise	<40dB(A) at 1m	TBD
Mass	<10kg	TBD
Dimensions	Stretch target - Unicase 4 / (261 x 300 x 135mm)	TBD
AC input	220-240V, 50Hz, 5A	Yes

Materials cost	<£1500	Yes